## Slide 1: IMPACT: A Substantial Upgrade to the HIPA Infrastructure at Paul Scherrer Institute
Daniela Kiselev :: 8100 :: Paul Scherrer Institut
R. Eichler, M. Haj Tahar, M. Hartmann, K. Kirch, A. Knecht, A. Koschik, D. Laube,
N. van der Meulen, T. Rauber, D. Reggiani, R. Schibli, J. Snuverink, U. Wellenkamp,
H. Zhang
Int. Conf. on Cyclotrons and their Applications (Cyc2022), Beijing, China, 5-9.12.2022, online

## Slide 2
Accelerator Facilities at PSI
p-Therapy (PROSCAN)
Comet: 250MeV, <1A
Swiss Light Source (SLS)
2.4GeV, 400mA
High Intensity Proton Accelerator (HIPA)
590 MeV, max. 2.4mA
SWISSFEL
5.8 GeV
Central control room
SINQ Spallation Neutron Source
UCN

## Slide 3
The PSI Proton Accelerator Facilities
HIPA (High Intensity Proton Accelerator)
- CW (50.63 MHz), 590 MeV,
- up to 2.4 mA(1.44 MW)
2 meson production targets
7 secondary beam lines
- SINQ and UCN spallation source
Page 3
PROSCAN (Proton therapy): since 2007
Comet: superconducting cyclotron
CW, 250 MeV, up to 1 mA protons
medical treatment:
3 Gantries, 1 Eye Cancer Treatment Station
Irradiation Station: PIF
PIF
hot cell HIPA
Gantry 1, 2 3
Target M
Comet
Target E
Spallation neutron source SINQ
Injector II
Injector I
ECR-source &
Cockroft-Walton
OPTIS
Ring
UCN

## Slide 4: Present TgM station (built 1985)
p
p
Beamlines under 22.5o
 optimized for high-momentum p > 100 MeV/c,
@ 350 MeV/c: π+::2x108 /(s mA)
PiM3
PiM1
particle physics
mSR (GPS, FLAME)
107 m+/s
nowadays
surface muons
needed
Target: graphite
2 mm thick rim
effective 5 mm (due to angle),
cooled by thermal conduction
no problems with bearings, since well shielded!
Notes: PiM1: mainly detector tests

## Slide 5: IMPACT = HIMB + TATTOOS
Isotope and Muon Production with advanced cyclotron and target technology
Upgrade of target station M to target station H for 100 x more surface muons
 HIMB
New target station for producing radioisotopes for reasearch in cancer therapy
 TATTOOS
Conceptional Design Report
https://www.dora.lib4ri.ch/psi/islandora/object/psi%3A41209
~ 100 people are involved
9 subprojects and 35 working groups
77 M project, 60 M by Swiss Roadmap for Research Infrastructure
1. evaluation passed in July 2022: best marks!
2. evaluation in Dec. 22
Notes: better statistics to lower the limit for forbidden particle decays (μ+ → e+γ )
higher rates to examine the (magnetic) properties deeper under the
surface of the material

## Slide 6: HIMB: High Intensity Muon Beams
Particle & material physics (mSR)
Surface muons (~ 28 MeV/c) rates of 1010/s for
Increasing the sensitivity for the
detection of rare muon decay
 Physics beyond the standard model
Study of magnetic properties below
surface with more sensitivity
Keep the competiveness
for future experiments &
attractiveness for users
Seite 6
A. Signer
 HIMB
Forbidden decay channels
590 MeV
28 – 120 MeV/c
Production of muons:
Graphite
target
Notes: ca. 100 mu.m below surface mit 28 MeV/c muons
more intensity
 shorter meas. times, ev. multiple probes, statistics deeper in the material

## Slide 7: TATTOOS: Targeted Alpha Tumour Therapy and Other Oncological Solutions
Life science:
Producing enough radioisotopes with 590 MeV p (100 mA)
for cancer treatment & diagnostics (theranostics) in quantities needed
for clinical studies on human beings
research only, no commercial production planned.
IP2 (72 MeV)
155Gd target
TATTOOS
590 MeV protons on Ta

## Slide 8: HIPA with HIMB and TATTOOS
Tattoos
HIMB
This is the
60 t crane
590 MeV
Ring cyclotron
UCN
pM3 mH3
pM1 mH2
particle physics:
2 separators to remove positrons
for mSR:
contains spinrotator
Both secondary beamlines are optimized for
low energy «surface» muons (~28MeV/c)

## Slide 9: View in the experimental hall
present TgM,
to be replaced by TgH(IMB) remote handling
Besides the shielding a lot of infrastructure has to be removed, e.g. He cryo station
and the water cooling loop (below cryo station)
and later built-up
power
supplies

## Slide 10: Concept for new target station HIMB at TgM
short wide solenoids with large fringing field in high radiation area
close distance to the target +/- 250 mm
thicker target (20 mm instead of 5 mm)  higher losses & activation
slanted target type
beamline optimized for large transmission of surface muons
& small losses of the proton beam
up to 0.45 T field
larger rim (> 100 mm)  larger surface
large rotating wheel for cooling
small angle relative to beam
capture
solenoid
graded-field
design
HIMB = High-Intensity Muon Beams
goal: 1010 surface muons/s
for particle physics
conceptional & techn. design already advanced
Notes: and beam spot size sigma < 50 mm at final focus in experimental area

## Slide 11: Beamline simulations from TgM/H to SINQ
Fixing aperture & positions of 3 collimators
fringing field at Target H included
non-pencil realistic beam profile before Target H/M
sensitivity studies of non-perfect beam
TgM/H
SINQ
TgE
AHL
Complete Beamline from Ring to SINQ in BDSIM by building GDML files,
some parts (targets, collimators) from CAD
Moving from 5 mm to 20 mm target:
Does the remaining beam line stand the losses?
Is the transmission acceptable?
Can the fringing field from the close capture solenoids corrected?
Can the beam profile required at TgE & SINQ target be fulfilled?

## Slide 12: Intensity-dependent beam conditions
The beam is injected into the cyclotron chain using a movable collimator (KIP2)
Radial probe measurement at the extraction of the PSI 590 MeV cyclotron (June 2021):
Normalized bunch intensity
14 mm
Extraction septum
Intensity [a.u.]
Radius [mm]
Beam current [mA]
0 0.5 1 1.5 2 2.5
sx [mm]
Energy deposition on the components and losses depend on the current.
Successful benchmarks of present beamline and BDSIM
measurements

## Slide 13: Beam envelope for 5 mm and 20 mm Target
Very good agreement between simulation and profile measurement for 5 mm TgM.
Optics tweaked in TgM-TgE region to minimize beam losses.
Energy spread after TgE about a factor of 2 larger for HIMB.
Optics tweaked by after TgE (strength of Quads).
SINQ
Ring
Transmission
5 mm Target
20 mm Target
Transmission ~ 67 %
(main losses before TgE)
horizontal
vertical
M. Haj Tahar, D. Kiselev, A. Knecht, D. Laube, D. Reggiani, J. Snuverink:
NIM A1046, 167638 (2023)

## Slide 14: TATTOOS: Building variants
14 x 16 x 16
13 x 16 x 8
WMFA
WEHA
31 x 16 x 16
WEHA
~ 50 % larger
but half of cellar will be kept
(D2 water tanks for UCN &
entry to active cooling station)
Up to 14 m deep,
difficult & expensive due
to small space & close to
fundament WEHA
Lots of infrastructure for HIPA, UCN, PROSCAN, SULTAN
have to be removed before start of construction
V1: small & deep
V2: long & flat
Several rebuildings
UCN-D2 reservoir,
UCN He buffer tank
UCN electr. infrastructure
UCN control room
WEHA transformers
PROSCAN ventilation
SULTAN media pipes
waste water pipes etc

## Slide 15: Time schedule
2023
2024
2025
2026
2027
2028
2029
2030
SD
Beam OP
SD
Beam OP
Long Shutdown
Beam OP
SD
Beam OP
SD
Beam OP
SD
Beam OP
SD
Beam OP
HIMB
TATTOOS
Techn. & Mechanical Design, Engineering, Planning
Procurement & Testing
Remove TgM
Installation
Comm. Pilot Exp.
Consolidation
User Operation
Techn. & Mechanical Design, Engineering, Planning
Procurement & Testing
Installation
Comm.
Bldg. Planning
Bldg. Tender
Bldg. Construction
Prep.
Prep.
1st Beam
1st Beam
TATTOOS: New building necessary  Realization 2 years after HIMB
Advantages:
Target installation for HIMB and TATTOOS not at the same time
less shortage on storage place for new components, shielding
more PSI resources available, less temporary hired staff
HIPA: 2027 no beam
Installation of HIMB
2028 first beam with new target station H

## Slide 16: Beamline to TATTOOS and operation modes
Quasi-parallel beam operation, i.e. no beam to TATTOOS, if pulse to UCN
~ 15 % beam time loss for TATTOOS (acceptable)
Quadrupole
Steering magnet
Profile monitor
EHT
ABS
Ionization chamber
Splitter: made for max. 20 mA
used for Piotron, Pyrex
Olivo, M., Mariani, E. and Rossetti, D.
An electrostatic beam splitter for the
PSI 590 MeV - 1MW proton beam line (1998).
TATTOOS Target:
10 cm Ta (Phase 1),
later U or Th
Target H, E & SINQ
UCN
Beam operation:
mode 1: SINQ & TATTOOS
 100 mA split from main beam to TATTOOS (ABT off)
mode 2: UCN
full beam (~ 2 mA) swept to UCN by fast kicker magnet (ABT on)
ABT
Kicker
AHK
wobbler

## Slide 17: Splitter
175 stripes out of a W-alloy
size: 2 mm x 50 mm
2 cathodes operating with 172 kV
deflection: +/- 1.5 mrad
Splitter geometry in ANSYS (H.Zhang)
Electric field map,
resolution :
25 µm by 3000 µm by 500 µm
First 3 stripes measure the current.
For protecting the splitter from damage:
current limit on stripes was set by comparing to the splitter EXT
used at 72 MeV for the isotope production simulations

## Slide 18: Result of splitter test
max. allowed current on strips
2023: larger beam optic with water cooled quadrupoles should be possible
As expected: larger losses about a factor 2
 dose rate measurements above proton beam line are analyzed
critically, since the beamline is maintained hands-on
 further measurement (dose rates) & simulations needed
average split current [mA]
average current on strips [mA]
80 mA beam could be split off
with horizontally increased
beam optics!

## Slide 19: TATTOOS target station
Courtesy C Sattler
Coupling of target
to media supply
Splitter
UCN
Courtesy V. Vrankovic
Wobbler
3 hot cells
Target
exchange
hot cell
Mass
separator
(magnet)
Separation of ions
by RILIS (Resonance Ionization Laser Ion Source)
& ISOL (Isotope Separation Online)
& chemistry
Clinical preparation (radiolabeling) in clean room (GMP),
collaboration with University hospital Zurich (USZ)
Beam profile on 10 cm Ta
 challenging to cool

## Slide 20
Summary
Introduction to the PSI High Intensity Proton Accelerator (HIPA)
Extraction from the Ring Cyclotron
Beam transfer to the meson production targets M/E and SINQ spallation source
Beam diagnostics for setup & optimization
Feasibility study of beam rotation for SINQ
Beam switchover to the UCN source
Conclusion
Page 20
IMPACT: a 77 MCHF project to upgrade the existing meson production station M
& a new target station to produce radioisotopes with 590 MeV protons
- covers a broad field of applications: particle, solid state physics, life science ......
- to be realized in 2027 to 2030
- CDR finished end of 2021, TDR planned for end of 2024
Thank your for your attention!