## Slide 1: GANIL: from the beginning 40 years ago to recent results and prospective
Savalle, C. Berthe, P. Chauveau, M. Dubois, B. Jacquot, O. Kamalou, G. Sénécal
And the GANIL staff

## Slide 2
A few days (and 40 years) ago : First beam from SSC2
November 19th, 1982 :
Output C02 : 2 µA
200 nA ejected from CSS1
Ar4+ stripped into Ar16+
4h : 150 nA entrance SSC2
7h15 : 15 nA accelerated
12h30 : 5 nA ejected from CSS2

## Slide 3
1973 :
1975 :
Design
1977
Final design
Notes: 2 CSS, + 1 tandem
Compact : experimental rooms in the same building aire expérimentales dans le même bâtiment

## Slide 4
The building of the facility (1978 – 1982)

## Slide 5
Beginning of operation
1983
1988
January 1983 :
1st experiment
mean availability in 1983 :
56 %
1st beams :
16O @ 95 MeV/A
20Ne @ 44 MeV/A
40Ar @ 27, 44 and 60 MeV/A
84Kr @ 35 MeV/A

## Slide 6
  The stripping efficiency was very bad at the beginning :
  Maximal energy 45 MeV/A for Kr, 25 for Xe (heavier beam accelerated)
  increase of the injection radius of SSC2 => increase of SSC1 energy
  New harmonics : SSC1 5 (previously : 7), SSC2 2
1989: Opération Augmentation de l’Energie (OAE project)
New injection elements in SSC2
After OAE : Kr @ 60 MeV/A, Xe @ 50 MeV/A, U @ 24 MeV/A
11th int. Cyclotron conference
Jacques Fermé (left)

## Slide 7
Ion sources Evolutions
PIG
ECR on injector 2 (C02) : 1985
100 kV platform on injector 1 (C01) : 1992
2004 : beam pre-selection
Inside platform

## Slide 8
The first radioactive beams : SISSI
cooled, rotated target (1 KW deposited power)
Two superconducting solenoids

## Slide 9
To high intensity : the THI project : 6 kW
December 2001 :
36Ar 95 MeVA,
26 µA (5 kW)
Beam loss monitors
Second Rebuncher
New SSC2 deflector

## Slide 10
  1995 – 1998 : SPIRAL 1

## Slide 11
1997 - 1998 : 1st beam tests in CIME
December 22th, 1997 : 1st beam accelerated
Very low intensity measured on the radial probe between the two parts of the deflector
But it was not the beam ! (the radial probe moving through the electric field measures a current without beam)
It was understood that the magnetic field was not equilibrated in the 4 sectors :
Installation of magnetic coils to compensate this effect
15 /11/ 1998 : 1st stable beam ejected
Les tests de CIME
sept 27th, 2001 : 1st radioactive beam

## Slide 12: 1989 : SME
2002 : IRRSUD
2005 : LIRAT

## Slide 13: 2018 : New SPIRAL1
Room 15
Cave
Charge
breeder
Injection
chamber
Extraction
chamber
TISS
Toward
post
-
acceleration
Primary
beam
Extraction
chamber
Magnetic
separation
Target
Concrete
Low
energy
beam
line
1+ or N+
ion
beam
FEBIAD 1+ Source
Charge breeder
Different Targets, up to Nb, with C Beam
Further requirement : Still possible to use ECR N+ source, beam passing through the booster
Non selective source : Mg, Ca, Sc, Cr, Mn, Co, Ni, Cu, Zn, Ga, Ce, As, Se, Al
But no acceleration by CIME (Q/A too low)

## Slide 14
SPIRAL2 Project
2005 : Project launched
2011 : excavation
Original project, including post-acceleration of fission products in CIME
2015: 1st beam in RFQ
October 28th, 2019 : 1st beam in the LINAC
SPIRAL2

## Slide 15: OPERATION 1983 – 2022 (cyclotrons)
LINAC + CYCLOTRONS
2019 - 2021
Chart: années
| 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2021 | 2022
Operation time (hours) | 4034.6821 | 5055.5556 | 4754.2662 | 4833.8462 | 4531.2977 | 4766.7162 | 2671.4801 | 5682.4561 | 5534.7334 | 5332.3442 | 5416.5261 | 6189.1447 | 3296 | 5323.75 | 4205 | 4370 | 4888 | 5320 | 5534 | 5682.75 | 5603.75 | 5532.25 | 5725 | 5750 | 5086 | 4752 | 5048 | 4987.25 | 4151 | 2865.25 | 3132.5 | 4169.5 | 3436 | 3214 | 2905.75 | 2710 | 3027 | 2737 | 3016
Physics time (hours) | 1396 | 2639 | 2786 | 3142 | 2968 | 3208 | 1480 | 3239 | 3426 | 3594 | 3212 | 3763 | 1925 | 3319.25 | 2400.75 | 2505 | 2960 | 3158.5 | 2989.25 | 3665.25 | 3765.75 | 3351.75 | 4256.25 | 3936.75 | 3298.5 | 2983.25 | 3555.75 | 3386.5 | 3092.5 | 2026.5 | 1895 | 3011 | 2692.75 | 2265.5 | 2340 | 2024.75 | 2030.5 | 1641 | 1819.5
Chart: 
| 2018 | 2019 | 2020 | 2021
Cyclotrons + LINAC (hours) | 3210 | 3783 | 3439 | 5513
Physics time (hours) | 2024.75 | 2030.5 | 872 | 2401

## Slide 16
Chart: Failure rate
| 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2021 | 2022
Disponibilité machine | 0.11411 | 0.11064 | 0.097122 | 0.12481 | 0.064323 | 0.11911 | 0.13075 | 0.078283 | 0.058885 | 0.09404 | 0.067213 | 0.1027 | 0.16895 | 0.10797 | 0.081999 | 0.042393 | 0.041125 | 0.076288 | 0.15562 | 0.20597 | 0.26575
Failures (cyclotrons)
Mainly due to Water leak Inside the machine (cavity, injection elements, beam line – slits, diagnostics, …)

## Slide 17: And for the future ?
DESIR (Decay, Excitation, Storage of Radioactive Ions) Facility
RFQ cooler + High Resolution Spectrometer
(1/20000)
DESIR Experimental Hall
(low energy RIB)
S3 - DESIR and SPIRAL1 - DESIR
Beam Transfer Lines
Public Enquiry in March-April 2023
The French Safety Authority has authorized the construction
Construction should begin in June 2023
Beam lines are ready, waiting to be installed

## Slide 18: And for the future ?
Next years : Still more demand than time available for cyclotrons
LISE spectrometer with SSC2 beams
Post-accelerated SPIRAL1 new beams
Fusion reactions (SSC1 beams)
Industrial applications
Tomorrow : DESIR with SPIRAL1 (21Na, 23Mg, 33Cl, 37K, 39Ca, 41Sc …)
=> Cyclotrons to be still operated in 15 – 20 years

## Slide 19
Developments of secondary beams
1 : FEBIAD 1+ source
FEBIAD has been used in line in alkali mode : post accelerated beams : 38mK (2019), 47K (2021)
It has been fiabilized (cooling of the insulators) and many tests have been made
≈80 radioactive isotopes/isomers seen, including 50+ at post-accelerable intensities (>105pps).
36Ar@74MeV/A 850W beam -> 12C target |  |  | 
Masse | Isotope(s) | T1/2 (s) | rate@1200W
8 | 8Li | 0.84 | 1.00E+05
20 | 20Na | 0.4479 | 1.38E+06
21 | 21Na | 22.49 | 1.13E+07
 | 1H20F | 11 | 3.90E+04
23 | 23Ne | 37.25 | 1.43E+06
 | 23Mg | 11.3046 | 4.27E+06
24 | 24Ne | 202.8 | 2.18E+05
 | 24Na | 53989.2 | 9.29E+07
 | 24Na_m | 0.0202 | 2.87E+05
 | 24Al | 2.053 | 9.47E+02
25 | 25Al | 7.183 | 3.80E+04
 | 25Na | 59.1 | 8.67E+06
 | 25Ne | 0.602 | 6.52E+03
 | 25Na 100V | 59.1 | 8.00E+06
26 | 26Na | 1.07128 | 2.21E+05
 | 26Al_m | 6.346 | 9.22E+04
27 | 27Mg | 567.5 | 2.62E+06
28 | 28Al | 134.7 | 3.27E+06
29 | 29Al | 394 | 1.14E+06
 | 29Mg | 1.3 | 2.27E+03
30 | 30Al | 3.62 | 1.30E+03
31 | 31Cl | 0.19 | 8.05E+02
 | C19O | 26.91 | 1.92E+03
32 | 32Ar | 0.098 | 1.16E+03
 | 32Cl | 0.298 | 8.52E+04
33 | 33Ar | 0.173 | 9.81E+04
 | 33Cl | 2.511 | 2.21E+06
34 | 34Ar | 0.8438 | 7.02E+06
 | 34Cl | 1.5266 | 2.39E+07
 | 34mCl | 1919.4 | 7.90E+07
35 | 35Ar | 1.7756 | 1.54E+08
 | H34mCl | 1919.4 | 1.89E+07
84Kr@67MeV/A 10W beam -> 12C target |  |  | 
Masse | Isotope(s) | T1/2 (s) | rate@500W
80 | 80Rb | 34 | 7.13E+07
79 | 79mKr | 50 | 3.28E+07
 | 79Kr | 126144 | 6.39E+07
 | 79Rb | 1374 | 1.14E+07
 | 79mBr | 4.85 | 8.17E+06
78 | 78mRb | 344.4 | 1.98E+06
 | 78Rb | 1059.6 | 3.89E+05
 | 78Br | 387 | 4.69E+07
77 | 77Rb | 226.8 | 5.20E+05
 | 77Kr | 4275 | 2.81E+07
 | 77mBr | 256.8 | 5.29E+07
 | 77Br | 205344 | 7.59E+07
 | 77mSe | 17.36 | 3.08E+04
76 | 76Rb | 36.5 | 2.37E+04
 | 76Kr | 53280 | 7.21E+06
 | 76Br | 58320 | 6.00E+07
 | 76mBr | 1.31 | 1.53E+06
75 | 75Kr | 276 | 8.03E+05
 | 75Br | 5802 | 4.26E+07
 | 75Ga | 126 | 1.22E+04
 | 75Ge | 4966.8 | 1.98E+05
71 | 71Se | 284.4 | 2.63E+04
 | 71As | 235080 | 2.26E+07
 | 71Zn | 147 | 1.96E+04
 | 71mZn | 14256 | 1.67E+05
69 | 69As | 912 | 1.86E+05
 | 69Ge | 140580 | 1.39E+07
 | 69mZn | 49521.6 | 2.66E+06
 | 69Cu | 171 | 4.22E+04
68 | 68mCu | 225 | 7.03E+04
 | 68Ga | 4062.6 | 1.42E+07
67 | 67Ge | 1134 | 1.74E+05
 | 67Ga | 281810.88 | 4.42E+07
65 | 65Ga | 912 | 6.92E+06
 | 65Ni | 9061.884 | 4.53E+04
48Ca@60MeV/A 200W beam -> 12C target |  |  | 
Masse | Isotope(s) | T1/2 (s) | rate@700W
37 | 37S | 303 | 9.27E+04
42 | H41Cl | 38.4 | 3.50E+05
 | 42Cl | 6.8 | 3.23E+05
 | 42K | 44496 | 6.24E+08
43 | 43Cl | 3.3 | 6.84E+04
 | 43Ar | 322.2 | 3.92E+07
45 | 45Ar | 21.48 | 5.68E+06
 | 45K | 1038 | 4.95E+08
47 | 47K | 17.5 | 2.67E+08
Elements for which we observed radioactive isotope
Phase | Objectives Project | 2019 38mK9+ 9MeV/A | 2021 47K10+ 7MeV/A
1+ ionization | 10% | > 5% | >15%
1+ to N+ transport | 80% | >80% | >80%

## Slide 20
Klystron 14,5 GHz
0 - 600 W
Plasma in the Charge breeder heated by:
The historic fixed frequency Klystron
A variable frequency Travelling-Wave Tube Amplifier
TWTA 8 -18 GHz
0 - 200 W
Developments of secondary beams
2 : SPIRAL1 Charge breeder
L. Maunoury et al, Charge Breeder at GANIL: metal charge-bred elements, Journal of Physics: Conference Series 2244 (2022) 012066
Chart: Ne/Na
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Ne K292W He p83 | 7.2 | 5.7 | 5.5 | 7.7 | 13.5 | 14.5 | 11.6 | 13.1 | 1.3 | 0
Na 1+/N+ K292W H2 p121 | 0 | 2.71 | 1.21 | 5.1 | 6.87 | 13.96 | 17.2 | 12.63 | 4.65
Phase | Objectives Project | 2019 38mK9+ 9MeV/A | 2021 47K10+ 7MeV/A
Charge Breeding | 5-10% | 1.5% | 8%
Extraction N+ | 50% | 80% | 80%

## Slide 21: Renovation program
Pre project CYclotronsRENovation
Objectives of the project
  to keep the facility in operational conditions for at least 20 years
Cyclotrons and experimental caves
Power Supplies and Magnets
RF cavities and systems
Remote control
PLCs
Vacuum systems
Diagnostics
Production targets
Ions Sources
Infrastructures and utilities
Electricity Distribution
Cooling systems
HVAC
Buildings
Various networks (water, air, gas)
Computer Infrastructures
Safety / Security / Radioprotection Systems
Radioprotection devices (radiation detectors, active dosimeters, gamma spectrometers, …)
Access Management System
Fire Safety System
WHAT IS TO BE DONE ?

## Slide 22
The main topic : rf cavities
Risk : cooling circuit leak, unreachable for repairing
        At least, manufacturing of a new cavity and keeping an old one as a spare : Reference scenario
        Replace the 4 SSC RF cavities : HIGH scenario
Issues to be assessed
  Sourcing
    At least one company able to manufacture a SSC RF cavity
    Evaluated cost : 5,7 M€ first cavity, 4 M€ each other
    Manufacturing delay : 2 years first cavity then 1 cavity per year
  RF characterization of the new cavity
    8 months
    No test stand available => qualification in a SSC cave
  Storage conditions of the spare cavity
  Handling issue : How to take a cavity out of a cyclotron cave and out of the building
New 2200 m² storage building
(not only for spare cavity)
40 years ago
assembly area

## Slide 23
Other major topics
REF scenario
~4 M€ 11,5 FTE
360 PS over 30 years old to refurbish or replace
  Power Supplies
REF scenario
~1,5 M€ 1,2 FTE
6 months of unavailability in 2026
Project Management Contract
  Cooling Systems
  Radiation detectors
REF scenario
~2 M€ 0,8 FTE
60 detectors to replace
  Remote control
REF scenario
~1,5 M€ 5 FTE
Code refactoring
VME crates virtualisation
Software engineering contract
  Storage building
REF scenario
~2 M€ 0,5 FTE
2200 m²
HIGH scenario
Not evaluated yet

## Slide 24: Conclusion
Thank you for your attention
After 40 years, GANIL cyclotrons are still demanded and it should be true for 20 years more
SPIRAL1 development is still active after the upgrade
DESIR : start of building construction in 2023
A large renovation plan is to be launched
In addition to the LINAC part (SPIRAL2) of the facility : operation, new experimental room, new injector to come