## Slide 1
High performance ECR ion sources development at RIKEN and their impact to heavy ion accelerators.
T. Nakagawa (Nishina center for accelerator based science, RIKEN)
Introduction
    RIBF and SHE search exp.
    Brief history
    Upgrade plan
Ion source
  Structure
  High temp. oven
Production of U ion beam(RIBF)
    Beam intensity (Consumption rate of material)
    Emittance ( Space charge effect)
Production of V ion beam(SHE)
    Beam intensity(consumption rate)
    Emittance and emittance slit
Conclusion and Next step
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)

## Slide 2
(II)RIKEN RIBF (P------ U)
I. RIKEN Radioactive Ion Beam Facility
2009~2018,U beam (X100)
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
N. Fukunishi, JPASJ 17 (2020)236
Two 28GHz SC-ECRISs

## Slide 3
(I)Synthesizing new elements(Z=119,120….)
Metallic ion beam
( Ti, V, Cr…..)
II. Synthesis of Super-heavy elements
V+Cm→Z=119(Super heavy element)
Small production cross section
Need intense beam
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
48Ca16+ for RIKEN RIBF
50Ti13+, 51V13+, etc for synthesis of super-heavy elements
M. Tanaka et al, JPSJ 91, 084201(2022)
Two 28GHz SC-ECRISs

## Slide 4
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
2007
2021
Brief history ( time revolution of beam intensity)
N. Fukunishi, JPASJ 17 (2020)236

## Slide 5
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
Upgrade plan (increase of the beam intensity)
28GHz SC-ECRIS
U35+ ion beam : >300emA
28GGHz SC-ECRIS
RILAC 2
The beam intensity of upgrade plan is 2pmA of U ion beam on target. To obtain this bema intensity, we need to produce at least 300 emA of U35+ ion beam from the ion source.
O. Kamigaito et al, Cylotron 2019, Cape Town, South Africa, MOB01

## Slide 6
High performance ECR ion sources development at RIKEN and their impact to heavy ion accelerators.
T. Nakagawa (Nishina center for accelerator based science, RIKEN)
Introduction
    RIBF and SHE search exp.
    Brief history
    Upgrade plan
Ion source
  Structure
  High temp. oven
Production of U ion beam(RIBF)
    Beam intensity (Consumption rate of material)
    Emittance ( Space charge effect)
Production of V ion beam(SHE)
    Beam intensity(consumption rate)
    Emittance and emittance slit
Conclusion and Next step
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)

## Slide 7
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
SC Solenoid coils
Hexapole magnet
Microwave guide
Movable biased disc
Beam extraction system
Plasma chamber
Iron yoke
Solenoid coil
Binj ~3.8T Bmin <1.0T Bext ~2.3T
Br ~2.1T
Plasma chamber : 15 cm (diameter)
50 cm (length)
Vacuum: 2x1100l/sec turbo pumps
(10-6~10-5 Pa)
Vext: <22kV
RF(18+28GHz): 28GHz(10kWmax)
18 GHz (~600W)
1.Movable biased disc
2.Movable extraction electrode
3.Solenoid coil ( focusing element)
Magnetic field and plasma chamber
G. D. Alton and D. N. Smithe, RSI vol. 65, 775(1994).
T. Nakagawa et al., RSI vol. 81, 02A320(1994).

## Slide 8
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
SC-magnet and cryostat
SC-Magnet
Cryostat
RILAC2 and RILAC:GM (~1.2 W at 4.2 K)
Additional ref.:
RILAC 2:GM-JT ref. (~4 W at 4.4 K)x2 ~8W
RILAC: GM-JT ref. (~4W at 4.2K) ~4W
Against the X-ray heat load produced in plasma

## Slide 9
High performance ECR ion sources development at RIKEN and their impact to heavy ion accelerators.
T. Nakagawa (Nishina center for accelerator based science, RIKEN)
Introduction
    RIBF and SHE search exp.
    Brief history
    Upgrade plan
Ion source
  Structure
  High temp. oven
Production of U ion beam(RIBF)
    Beam intensity (Consumption rate of material)
    Emittance ( Space charge effect)
Production of V ion beam(SHE)
    Beam intensity(consumption rate)
    Emittance and emittance slit
Conclusion and Next step
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)

## Slide 10
High temperature oven
RIKEN 28 GHz SC-ECRIS
RF injection side
High temperature oven
For production of the V and U vapour, we used the high temperature oven. To obtain enough temperature for evaporating the materials, the detailed simulation was carefully done and successfully obtained high enough temperature to produce the vapour.
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)

## Slide 11
Crucible (High temperature oven)
Old crucible : J. Ohnishi et al, Rev. Sci. Instrum. 87, 02A709 (2016)
New crucible: J. Ohnishi et al, in the proceedings of ECRIS2018
Vanadium powder
Ceramic crucible
(Y2O3 or Al2O3)
W crucible
Old crucible New crucible
10 mm
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
For long term operation, we fabricated new crucible, which has almost two times larger volume than the old one.
UO2 ~4gr
V ~2gr

## Slide 12
High performance ECR ion sources development at RIKEN and their impact to heavy ion accelerators.
T. Nakagawa (Nishina center for accelerator based science, RIKEN)
Introduction
    RIBF and SHE search exp.
    Brief history
    Upgrade plan
Ion source
  Structure
  High temp. oven
Production of U ion beam(RIBF)
    Beam intensity (Consumption rate of material)
    Emittance ( Space charge effect)
Production of V ion beam(SHE)
    Beam intensity(consumption rate)
    Emittance and emittance slit
Conclusion and Next step
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)

## Slide 13
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
Consumption rate
Consumption rate vs. Oven power
Beam intensity as a function of consumption rate at ~3 kW
The consumption rate increases exponentially with increasing the oven power from 600 to 900 W
The beam intensity of U35+ increases with increasing the consumption rate up to ~10 mg/h and than saturated at ~3 kW of microwave power. The beam intensity decreases with increasing the consumption rate above 20 mg/h

## Slide 14
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
U35+
U46+
Beam intensity of highly charged U ions as a function of microwave power
The beam intensity of highly charged U ions linearly increases with increasing the microwave power up to 3.5 kW. It is noted that the beam intensity is not saturated at highest power in this experiments.
We have possibility to further increase the beam intensity with higher microwave power.

## Slide 15
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
U33+
U35+
U46+
U50+
Microwave power ~3 kW
Charge state distribution

## Slide 16
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
Beam intensity of highly charged U ions as a function of microwave power
Microwave power dependence

## Slide 17
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
2007
2021
18GHz ECRIS
28GHz SC-ECRIS
~3emA
~180emA
Time evolution of the U35+ ion beam intensity
T. Nakagawa, JPASJ 4, 180,(2007)

## Slide 18
High performance ECR ion sources development at RIKEN and their impact to heavy ion accelerators.
T. Nakagawa (Nishina center for accelerator based science, RIKEN)
Introduction
    RIBF and SHE search exp.
    Brief history
    Upgrade plan
Ion source
  Structure
  High temp. oven
Production of U ion beam(RIBF)
    Beam intensity (Consumption rate of material)
    Emittance ( Space charge effect)
Production of V ion beam(SHE)
    Beam intensity(consumption rate)
    Emittance and emittance slit
Conclusion and Next step
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)

## Slide 19
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
Emittance vs. microwave power
U35+ ion
Emittance vs. extraction current
V13+ ion
U35+ ion
Emittance
It seems that the no relevance between the emittance and the microwave power
The emittance becomes larger with increasing the extraction current
(space charge effect?)

## Slide 20
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
=
Space charge effect
U35+ emittance <0.1 p mm mrad ?
=
Y. K. Batygin, NIMA 539, 455 (2005).
U35+
Space charge effect
To obtain more accurate value, we need the measured emittance at lower extraction current
Test experiments (Xe20+) for lower extraction current
Beam intensity of Xe20+ ~30emA
Ion source emittance
To obtain smaller emittance, we need lower extraction current

## Slide 21
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
Reduction of extraction beam current ( smaller emittance)
Ion trap
qV (charge state x potential dip)
Plasma potential
Plasma potential
Larger q strong trap central region
Existence of plasma potential dip
Beam size
Higher charge state
Lower charge state
Physics of Particles and Nuclei Letters, 2021, Vol. 18, No. 3, pp. 370–377
V. Mironov et al.,

## Slide 22
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
Extraction hole ( 10 mm in diameter)
Extraction beam is mainly O ions ( lower charge state)
We may reduce the extraction beam using smaller extraction hole
U ions
O ions
(2+~5+) Larger beam size
(31+~40+) Smaller beam size
If we use smaller extraction hole, the total extraction current may be reduced while keeping the beam intensity of U35+

## Slide 23
High performance ECR ion sources development at RIKEN and their impact to heavy ion accelerators.
T. Nakagawa (Nishina center for accelerator based science, RIKEN)
Introduction
    RIBF and SHE search exp.
    Brief history
    Upgrade plan
Ion source
  Structure
  High temp. oven
Production of U ion beam(RIBF)
    Beam intensity (Consumption rate of material)
    Emittance ( Space charge effect)
Production of V ion beam(SHE)
    Beam intensity(consumption rate)
    Emittance and emittance slit
Conclusion and Next step
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)

## Slide 24
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
Consumption rate of V and Ti ( High temperature oven)
To obtain metal vapor (Ti and V), we used the High temp. oven. To avoid the chemical reaction between the crucible and material (Ti and V), we used theY2O3 inner crucible.
The consumption rate increases exponentially with increasing the oven power. The consumption rate of Ti is much higher than that for V. it is due to the difference of the melting point.
Melting point of Ti: ~1670 K
Melting point of V: ~1940 K
J. Ohnishi et al, ECRIS2018, Catania, Italy, WEB4

## Slide 25
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
V13+ intensity(consumption rate vs. microwave power)
Double oven system ( metal V: 4 gr max)
One month operation without break
Microwave power :~2.4 kW
Consumption rate: ~4 mg/h
Microwave power :~1.4 kW
Consumption rate: ~ 10 mg/h
Many combinations of microwave power and material consumption rate to produce same beam intensity
T. Nagatomo et al, RSI 91, 023318(2020)

## Slide 26
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
V13+ ion beam – microwave power dependence, charge distribution-
The beam intensity linearly increases with increasing the microwave power up to ~3.5 kW. It should be stressed that the beam intensity is not saturated at highest power. Therefore we have possibility to obtain higher beam intensity at higher power.
We do not find strong peak of highly charged N ions in the spectrum to produce ~1mA of V13+

## Slide 27
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
70Zn15+,16+ ~50emA
~3pmA
Nh 19(+19, -10)fb (~150day/counts)
51V13+ ~1emA
~75pmA
Z=119 ? days/ counts
Zn ion beam(Nh production) vs.V13+ beam (Z=119 production)
The beam intensity of V13+ ions is over 20 times higher than that of Zn ion beam used to produce Nh (Z=113)
K. Morita NP A944 (2015)30

## Slide 28
High performance ECR ion sources development at RIKEN and their impact to heavy ion accelerators.
T. Nakagawa (Nishina center for accelerator based science, RIKEN)
Introduction
    RIBF and SHE search exp.
    Brief history
    Upgrade plan
Ion source
  Structure
  High temp. oven
Production of U ion beam(RIBF)
    Beam intensity (Consumption rate of material)
    Emittance ( Space charge effect)
Production of V ion beam(SHE)
    Beam intensity(consumption rate)
    Emittance and emittance slit
Conclusion and Next step
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)

## Slide 29
LEBT
Low Energy Beam Transport (LEBT) (I)
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)

## Slide 30
Emittance slit
Beam trajectory
For safe operation of intense beam for long term, it is important to minimize the beam loss in the accelerators. Therefore, we installed the emittance slits at the beam focus point (F1) which can cut off the beam in the phase spaces (x-x’ and y-y’)
Emittance Slit
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
T. Nagatomo et al, RSI 91, 023318(2020)

## Slide 31
High performance ECR ion sources development at RIKEN and their impact to heavy ion accelerators.
T. Nakagawa (Nishina center for accelerator based science, RIKEN)
Introduction
    RIBF and SHE search exp.
    Brief history
    Upgrade plan
Ion source
  Structure
  High temp. oven
Production of U ion beam(RIBF)
    Beam intensity (Consumption rate of material)
    Emittance ( Space charge effect)
Production of V ion beam(SHE)
    Beam intensity(consumption rate)
    Emittance and emittance slit
Conclusion and Next step
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)

## Slide 32
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)
Conclusions and Next step
Production of intense U and V ion beam with optimizing the consumption rate of the material (metal vapor)
  U33+ ~350emA
  U50+ ~20emA
  The beam intensity of U35+(28GHz SC-ECRIS) is about 100 times higher than that with 18GHz RIKEN ECRIS
  51V13+ ~1emA
  The beam intensity of V13+ ions is over 20 times higher than that of Zn ion beam used to produce Nh (Z=113)
2. It is not so difficult to produce 300emA of U35+ at present stage. The problem is that we need to install large amount of material in the plasma chamber ( 3or 4 oven system ?)
3. It seems that emittance size is affected by the space charge effect, especially extracted beam of the ion source
To reduce the emittance size, it is essential to reduce the extraction current.
Use of smaller extraction hole

## Slide 33
Cyclotron 2022 (Dec. 5-9, 2022, Beijing, China)