## Slide 1
Application Progress of CYCIAE-100 high current proton Cyclotron
Lei Cao
China Institute of Atomic Energy
The 23rd international conference on cyclotrons and their applications , 5-9 December 2022 ,Beijing

## Slide 2
Outline
Overview of BRIF and CYCIAE-100
Application and research
Conclusion
1
Notes: My presentation will cover the following five aspects: the first part is … second is …. Last is …

## Slide 3
Introduction to BRIF
(Beijing Radioactive Ion-beam Facility)
HI-13 Tandem
Super booster 2 MeV/q
ISOL
Quality resolution 20000
100 MeV Cyclotron 520uA
2
building 3775 m2 , total investments 365 M RMB, construction started in April 2011, completed in 2014, opening for user experiments in 2016.
The main performance indexes have reached the international leading level.
Notes: BRIF was started at CIAE in 2004. The project outline is shown in Fig. 1. It consists of a 100 MeV cyclotron, an isotope separator online system, modification of the existing tandem, a superconducting Linac booster, various experimental terminals, and an isotope production station

## Slide 4: BRIF Model
100 MeV
Cyclotron
HI-13 Tandem
100MeV/520uA H- AVF cyclotron(CYCIAE-100)；
Isotope Separator On-Line 20000 mass resolution（ISOL）；
After the tandem, a 2MeV/q superconducting linac booster（SCL）；
Multiple beam lines and experiment terminals.
multi-use of one device, combination of two devices, and combination of multiple devices
SCL
ISOL
3
Notes: BRIF was started at CIAE in 2004. The project outline is shown in Fig. 1. It consists of a 100 MeV cyclotron, an isotope separator online system, modification of the existing tandem, a superconducting Linac booster, various experimental terminals, and an isotope production station

## Slide 5
Introduction to CYCIAE-100
CYCIAE-100 ( a 100 MeV proton cyclotron)
On July 4th 2014, got first 100MeV/20µA proton beam from CYCIAE-100, awarded as Top10 scientific achievements of 2014 in China.
Productions of intense proton and radioactive ion beam (RIB) ,carrying out research on nuclear data, radiation effect, material and life sciences and medical isotope production etc.
Compact cyclotron 100 MeV /520 µA
Witness the cyclotron beam for the first time
4

## Slide 6: Introduction to CYCIAE-100
The largest compact AVF cyclotron in the world
Control room
Beam injection
100MeV
2022/12/6
5

## Slide 7: Introduction to CYCIAE-100
  High beam current -2pA-520uA max
  Beam energy range -70-100MeV
  High transport efficient- 99.9%
  Low operating cost
  Low magnification
  Simultaneously bio-extraction
  Multi-modes
2014年6月25日
First physic experiment(SEE ) in Nov. 2016(100 MeV、30nA)
SEE
Terminal
North beam line
South beam line
6

## Slide 8: 100 MeV Proton Cyclotron
Experiment Hall
Isotope production
ISOL target
Low Energy RIB hall
Neutron Source
SEE beamline
1nA-1uA
50uA
5uA
200uA
1uA-20uA
Cyclotron Hall
Proton & Quasi-monoenergetic energy Neutron Source
Five beamlines as follows:
Northward can supply beam to ISOL and isotope target station.
Southward can supply beams to three beam lines:
Intensity neutron target line(15m neutron tube and 30m neutron tube).
Single event effect test bench (nA level).
Proton and Quasi-monoenergetic neutron source.
7

## Slide 9
Outline
Overview of BRIF and CYCIAE-100
Application and research
Conclusion
8

## Slide 10: Application and research
Up to Dec, 2022，100MeV cyclotron has produced over 5000 hours beam time for users
Users from different area
Medical schools
Institutes for electronic and space technology
Universities
Institutes for nuclear physics
9

## Slide 11: Application and research
The Usage
of Cyclotron in our lab
Medical isotope production, proton therapy
nuclear physics research
Radiation effect Research
Medical and other applications
Nuclear reaction, nuclear structure
Proton , neutron SEE, radiation resist
10

## Slide 12: Application and research
Innovative achievements in radioactive nuclear beam physics
The highest quality Na-20 radioactive beam is produced by using high resolution ISOL device in 2015, and the strange decay mode of β-γ-α of 20Na (Sodium)is discovered for the first time in the world.
brought China's nuclear astrophysics, radioactive nuclear beam physics and other scientific research into the international forefront.
20Na energy spectrum diagram
24Mg(p,xpn)20Na
11

## Slide 13: Application and research
100MeV cyclotron achieved the design goal of 200 μA in 2018,
Then promote the beam current to 520uA max at last.
12

## Slide 14: Application and research
Quasi-monoenergetic neutron experiment
calibration of high energy neutron,a bottleneck restricting space neutron detection .
the quasi-monoenergetic neutron reference radiation field in the energy region above 20MeV is established, and the calibration technology of neutron spectrometer is studied.
China is the second country in the world with neutron reference radiation field and calibration ability in the energy region above 20MeV.
Be neutron target
3D sample platform
Beryllium
13

## Slide 15: Application and research
Quasi-monoenergetic neutron platform
The quasi-monoenergetic neutron target consists of three beryllium targets with thickness of 0.4mm, 0.5mm and 0.6mm and one fluorescent target.
Beryllium and beryllium oxides have strong chemical toxicity, so the quasi-monoenergetic neutron target is completely sealed and maintains a certain negative pressure. “
Prof. Li will give details in Session FRB-1.
Fission ionization chamber measurement signal
14

## Slide 16: Application and research
High energy neutron platform of Nuclear data
Continuous spectrum neutron nuclear data Measurement platform.
The construction of beam line and experimental terminal was completed in 2021.
Proton bombardment of tungsten target to produce neutrons
15

## Slide 17: Application and research
High energy neutron platform of Nuclear data
The co-axiality error between neutron collimation hole and neutron beam pipe is less than 0.10mm.
The collimator is composed of 35cm copper at the front end and 65cm iron at the rear segment.
four kinds of collimating aperture choices of 30mm, 60mm, 100mm and complete shielding.
16

## Slide 18: Application and research
High energy neutron platform of Nuclear data
Measurement of spectrum by double liquid scintillation neutron time-of-flight method
Neutron energy range is 3-100MeV
When the proton current is 1 μ A, the measured neutron Fluence in the energy region of 3 -100 MeV is about 3.28 × 10 E4 cm-2s-1.
 | 0-1MeV | 1-3MeV | 3-10MeV | 10-100MeV | Total
Theoretical | 3.53E4 | 2.59E4 | 1.90E4 | 0.74E4 | 7.95E4
 | 44.4% | 32.6% | 23.9% | 9.3% | 100%
Experimental | / | / | 2.87E4 | 0.41E4 | 3.28E4
 | / | / | 87.6% | 12.4% | 100%
Comparison between theoretical and experimental values of neutron spectrum (1 μ A proton)
17

## Slide 19: Application and research
High energy neutron platform of Nuclear data
The first neutron single event effect (SEE) experiment was carried out using neutron beam line.
Three kinds of SRAM devices with different characteristic sizes were tested by single event reversal (SEU).
the beam from ion source was pulsed as 5MHz， Experiments related to pulsed neutron beam can be carried out, which greatly improves the research conditions of continuous spectrum in China.
18

## Slide 20: Application and research
Radiation dose measurement
purpose: proton beam water absorbed dose determination technology, measure the proton beam water absorbed dose absolutely and relatively in two ways
establishing the proton beam water absorbed dose transfer system, and provide measurement technical support for astronaut proton dose monitoring.
results: measurements of water absorbed dose of proton beam were completed(0.8Gy/min, 1nA).
19

## Slide 21: Application and research
Biological and medical experiments irradiated by protons
In the face of complex space radiation environment, Proton radiation has an important effect on the life and health of astronauts of space mission.
The batch of important data of intestinal microflora of mice irradiated by intermediate energy proton were successfully obtained and confirmed for the first time that proton irradiation had an effect on intestinal microflora in mice.
enhance the health protection ability of astronauts, which will provide a solid scientific and theoretical support for the smooth promotion of China's deep space exploration.
20

## Slide 22: Application and research
Biological and medical experiments irradiated by protons
Radiotherapy , a common method for the treatment of cancer. FLASH imaging is delivered at an ultra-high dose rate (> 40Gy/s), Reducing the normal tissue toxicity .
on the N3 line of 100MeV cyclotron, three-dimensional water phantom PTW, Bragg peak ionization chamber , reference ionization chamber and finger ionization chamber were used for dose measurement.
The ultra-high dose rate of 40.76Gy/s (204.9 for 5 second) is obtained in this test, which can be used in the study of proton FLASH.
21

## Slide 23: Application and research
Isotope production experiments irradiated by protons
The first production of Ac-225 with 100MeV cyclotron in China
Through the design and research of isotope solid target system, a high power solid target radionuclide experimental device has been successfully developed, and core technologies have been mastered.
It has laid a solid foundation for the research of other nuclides related to the production of accelerators.
225Ac-221Fr:
218.2keV characteristic ray
22

## Slide 24
Beam profile：1~10cm
distribution：75%
Injection rate： 1E8 max
Proton energy range：90、80、70、
60、50、40、 30
Sample platform：51cm*51cm
Rotation angle：<65 deg
Collimator opening ：0~10cm，60mm thickness
Experimental samples: SRAM, FPGA, SoC and other electronic components
Proton initial energy：100 MeV
SEE Proton line Phase I
Quadrupole
slit
Vacuum valve
Scattering target
monitor、FC
Titanium film
Ion chamber
Degrader set
collimator
Sample platform
beam dump
Moving laser
Faraday cup
Test system area
Experiment hall
XY steering
23

## Slide 25
SEE Proton line Main parts
Quadrupole
slit
Vacuum valve
Scattering target 1 & 2
monitor、FC
Titanium film
Ion chamber
Degrader set
collimator
Sample platform
beam dump
Moving laser
Faraday cup
Experiment hall
XY steering
XY steering\Quadrupole\slit+FC
24
Notes: The proton single event effect irradiation device is mainly composed of five systems: beam lowering system, beam scattering system, energy degrader system, beam diagnosis system and sample platform.

## Slide 26
SEE Proton line Main parts
Quadrupole
slit
Vacuum valve
Scattering target 1 & 2
monitor、FC
Titanium film
Ion chamber
Degrader set
collimator
Sample platform
beam dump
Moving laser
Faraday cup
Experiment hall
XY steering
XY steering\Quadrupole\slit+FC
Quadrupole
Quadrupole
X
Y
Beam lowering system
25
Notes: The cyclotron is a strong current accelerator, which generally provides an initial current of the order of uA, while the single particle effect experiment generally requires a weak beam of nA level, so it is necessary to reduce the proton beam intensity.
Therefore, the effect of beam reduction can be achieved by using a quadrupole lens to disperse the beam in the X and Y directions, and then intercept a small part of the beam in the center through the slit.

## Slide 27
SEE Proton line Main parts
Quadrupole
slit
Vacuum valve
Scattering target 1 & 2
monitor、FC
Titanium film
Ion chamber
Degrader set
collimator
Sample platform
beam dump
Moving laser
Faraday cup
Experiment hall
XY steering
Beam scattering system
26
Notes: The original beam spot provided by the accelerator is generally small, while the single particle effect experiment generally needs a uniform large beam spot to cover the whole electronic chip, so it is necessary to enlarge the beam spot size.
Therefore, by using the method of beam expansion by double scattering targets, the proton beam forms a Gaussian distribution after passing through the first scattering target, and then passes through the second scattering target, because the heavy nuclear material in the center has stronger scattering ability and has a stronger weakening effect on the beam current. after a certain flight distance, a large area uniform beam spot can be obtained in the sample plane.

## Slide 28
SEE Proton line Main parts
Quadrupole
slit
Vacuum valve
Scattering target 1 & 2
monitor、FC
Titanium film
Ion chamber
Degrader set
collimator
Sample platform
beam dump
Moving laser
Faraday cup
Experiment hall
XY steering
Beam degrading system
27
Notes: Accelerators can only provide proton beams with initial energy of 75-100MeV, while single-particle effect experiments generally need proton beams with a wide energy range to measure a more complete cross-section curve, so it is necessary to reduce proton energy.
Therefore, by placing a group of energy-reducing sheets with accurately calculated thickness on the beam line, the fast switching of proton beams in a certain energy range can be realized by the combination of multiple energy-reducing sheets.

## Slide 29
SEE Proton line Main parts
Quadrupole
slit
Vacuum valve
Scattering target 1 & 2
monitor、FC
Titanium film
Ion chamber
Degrader set
collimator
Sample platform
beam dump
Moving laser
Faraday cup
Experiment hall
XY steering
Beam diagnosis system
28
Notes: In order to carry out the single particle effect experiment, it is necessary to measure the beam parameters such as proton irradiation Fluence and uniformity.
The proton beam flux is measured by on-line monitoring of transmission ionization chamber, plastic scintillator detector or Faraday cup.
The plastic scintillator detector is used at low injection rate and the Faraday cup is used at high injection rate.

## Slide 30
SEE Proton line Main parts
Quadrupole
slit
Vacuum valve
Scattering target 1 & 2
monitor、FC
Titanium film
Ion chamber
Degrader set
collimator
Sample platform
beam dump
Moving laser
Faraday cup
Experiment hall
XY steering
Sample platform
2525cm2
2525cm2
2525cm2
Beam diagnosis
range：500mm*500mm
29
Notes: Multi-dimensional sample platform:
range: 500mm*500mm.
Sample rack removable.
For device-level and machine-level testing, need to prepare 50cmx25cm backplane in advance.

## Slide 31
quadrupole
Vacuum isolation film
Al degrader set
Sample platform 1&2
Beam dump
Scattering target
Switch magnet
Bending magnet
SEE Proton line Phase II
Beam energy：10-100 MeV
Injection rate：1E6-1E10 /cm2.s
Beam drop: defocus + slit.
Energy reduction: energy reduction tablet.
Beam expansion: multi-stage field
Beam diagnosis：SC+FC
DUAL platform to improve efficiency
30

## Slide 32: Application and research
Background: cell density of devices in the circuit continue to increase, the range of radiation of a single particle can cover multiple devices. Furthermore, the charge collection effect is caused by multiple nodes in the circuit, and the displacement effect is produced in the circuit.
0.25μm 8×512k×8bits CMOS SRAM
CIAE first SEE experiment
31

## Slide 33: Application and research
Space environment radiation effect
Result: the CMOS device has a shift effect when the proton irradiation flux is 2E11 , and the overall performance of the device decreases with the emergence of the displacement effect.
the space proton has a displacement effect on aerospace CMOS devices, which should be considered and strengthened in the practical application environment.
0.25μm 8×512k×8bits CMOS SRAM
CIAE jointly carried out the first experiment on the proton single event effect in Nov. 2016, Fill the gap in the anti-radiation experiment of intermediate energy protons in China.
32

## Slide 34: Application and research
Innovative achievements in radioactive effect
LHC鸟瞰图
CEPC Model
LGAD chip， 2.6mm*2.3mm
Detector profile
Time resolution of two low-gain avalanche amplified silicon sensors is lower than 30ps after irradiation with contrast to Spain and Japan about 50ps
33

## Slide 35: Application and research
Innovative achievements in radioactive effect
LHC鸟瞰图
Experimental verification of key technologies of LHC/ATLAS single crystal diamond detector
LHC birdview
ATLAS Calorimeter
Proton irradiation of single crystal diamond module; Radiation protection effect of typical materials for manned spacecraft
34

## Slide 36: Application and research
Biological and medical experiments irradiated by protons
First dual extraction beam for users
Effects of proton irradiation on oxidative damage of mitochondria in tumor cells with 1 pA at S3
single crystal diamond experiment with 300 nA at N1
35

## Slide 37: Application and research
Innovative achievements in radioactive effect
0.18 μ m mixed signal integrated circuit
Objective: to verify its resistance to proton irradiation, compare the experimental results of protons and heavy ions, and study the radiation damage mechanism of 0.18 μ m CMOS devices.
Results: the four devices reached the total dose of 5E10 in turn, and no obvious SEL and SEFL occurred.
Study on single event effect of 14nm and 65nm SRAM integrated circuits
Results: the function of the main control FPGA is abnormal.
36

## Slide 38: Application and research
Biological and medical experiments irradiated by protons
Sensitivity of nasopharyngeal carcinoma and glioma to proton irradiation.
A375 cancer cells were irradiated by proton to study the changes of cell survival rate, cell cycle change, apoptosis and DNA damage with dose.
37

## Slide 39
Outline
Overview of BRIF and CYCIAE-100
Application and research
Conclusion
38

## Slide 40: Conclusion
CYCIAE-100 facility as the core of BRIF, is playing more and more important role in the nuclear data, radiation effect, agriculture, medical and isotope production area.
We will continue to improve the performance and efficiency of the accelerator, complete the upgrading of aging devices, and maintain the stability of the beam.
In the future, it is planned to continue to expand the facility capacity, give full play to the potential of large scientific devices in the application of accelerator neutron sources and Nuclear waste transmutation(ADS), and make vital contributions to the promotion of the country's scientific and technological strength.
39

## Slide 41
Thank you !
40