## Slide 1: On the Energy Limit of Compact Isochronous Cyclotrons
Wiel Kleeven - IBA

## Slide 2: Main goal of this study
We use a general Hamiltonian approach, to find formulas for the energy limit Emax of compact isochronous cyclotrons.
They will be helpful in preliminary and conceptual design studies for defining the following parameters:
  The rotational symmetry number N of the magnetic sectors
  The maximum spiral angle  of the sectors
  The flutter F
The limit is assumed to be determined by two competing requirements:
  To have sufficient azimuthal field variation to garrantee stable vertical motion
  To have a not-too-high azimuthal field variation to avoid the stopband of the linear structural resonance 2nr=N. (a resonance that can not be crossed).
Other resonances due to magnetic field imperfections are not considered.

## Slide 3: General remarks
This paper pays tribute to and is inspired by my PhD thesis promotor prof. Henk Hagedoorn; it is an application and generalization of his well-know publication:
  Ref. 1: H. L. Hagedoorn and N. F. Verster, “Orbits in an AVF Cyclotron”, in Nuclear Instruments and Methods, vol. 18,19, pp. 201-228, 1962.
The derivation is too elaborate and too complex to show in detail in this presentation. We present here a strongly compressed version. The full derivation and results can be found in the following two publications:
  Ref. 2: W. Kleeven, Energy limit of compact isochronous cyclotrons, 2022, arXiv:2211.01029
  Ref. 3: W. Kleeven, On the Energy limit of compact isochronous cyclotrons, Accepted for publication in the Journal of Instrumentation (JINST) as contribution to a special issue of the ICFA (International Committee for Future Accelerators) newsletter #84 on: Dynamics of High Power and High Energy Cyclotrons.

## Slide 4: Main assumptions and approximations (1)
We solve the static motion (no acceleration)  P=P0=constant
No field errors (perfect N-fold rotational and median plane symmetry)
Motion is solved near a radius r0 defined by: and
Reduced magnetic field:
Where f(,r), the normalized azimuthal field variation, is considered as small:
  First important approximation:
Therefore our limitation to « compact » cyclotrons (as compared to SSC’s)
results derived up to O(f2)

## Slide 5: Main assumptions and approximations (2)
The AVF function f is expanded in a Fourier series:
And the reduced field is Taylor expanded:
with normalized average field derivatives:
We assume that the magnetic field is perfectly isochronous. Then can be expressed in the relativistic g parameter

## Slide 6: Main assumptions and approximations (3)
An important generalization wrt the HV-study is that we do not consider as small, because the half-integer resonance stopband happens at relativistic energies. We therefore have to keep cross-terms between and the Fourier-terms An,Bn. This complicates the derivation considerably.
HV-non-relativistic zone

## Slide 7: Main assumptions and approximations (4)
The particle motion is mainly determined by the dominant Fourier term CN. To simplify our final results we express the higher harmonics in terms of the dominant contribution, by assuming a hard-edge profile for f(q,r), with equal hill and valley width. For this we find:
The flutter of this profile is:
In this way, all Fourier coefficients can be expressed in the same flutter function:
This is the second important approximation in the derivation

## Slide 8: Method of derivation (1)
We start with a general form of the cyclotron Hamiltonian in polar coordinates.
We decouple the horizontal/vertical motions by assuming that the horizontal motion is in the median plane and the projection of the vertical motion follows the Equilibrium Orbit (EO).
This gives two separate Hamiltonians; Hx for the horizontal and Hz for the vertical motion.
The EO is found as the periodic solution of Hx and is expressed in a Fourier series as function of the independent variable q.
New canonical variables wrt the EO are introduced and the Hamiltonian Hx is Taylor expanded with respect to these new variables
Only terms up to 2nd degree in the canonical variables need to be kept. This corresponds to linear motion and is sufficient as the half-integer resonance 2nr=N is linear.
By 2nd canonical transformations, Hx and Hz are brought to the normal form:
(A)

## Slide 9: Method of derivation (2)
Here the parameters n0x and fx(q) depend only on the reduced magnetic field quantities.
The term n0x is O(f0) and the term fx(q) is an oscillating term of O(f1) (zero average)
We first solve the above Hamiltonian (A) in a general way.
For that we design a third linear canonical transformation, that moves the oscillating part fx(q) to new terms of the next higher order O(f2). Within our required level of approximation, we only have to keep the average of these new terms.
This transformation solves the motion (upto O(f2)) as H becomes independent of q
The betatron tunes of the (horizontal or vertical) motion become:
Here cn are the Fourier amplitude coefficients of fx(q).

## Slide 10: Method of derivation (3)
For the derivation of the 2nr=N resonance we study the motion by introducing action-angle variables in a phase space that rotates with frequency N/2. and then move the oscillating part to the next higher order O(f2).
The lower and upper stopband limits are obtained as:
Here n0x and cn must be expressed in terms of the reduced magnetic field parameters.
The O(f2)-parts in n0x and n0(1,2) have the following general form:

## Slide 11: Method of derivation (4)
We simplify the above expression by the following steps:
  Assume that the harmonic phase derivatives ’n do not depend on n (valid for at least the first five harmonics)  ’ can be taken out of the summation.
  Express Fourier coefficients Cn in terms of the flutter F and take out of summation.
  Express average field derivatives µ’, µ’’, µ’’’ in terms of relativistic g (perfect isochronism)
  Sum up the series analytically
  The O(f2)-parts are thus transformed to the simpler form:

## Slide 12: Results (horizontal tune)
Horizontal tune:
A cyclotron design template was made in excel. The first 3 columns pasted in by the user:
  radius r
  flutter F
  the azimuth  of the center of the magnetic sector
And three constants:
  the number of sectors N
  the particle revolution frequency frev
  the central field B0
The template calculates all results derived here:
  Tunes, resonance stopband, Biso, relation g=g(r)

## Slide 13: Benchmark against IBA/NHa C400 carbon therapy cyclotron (1)
Invited talk THBI1
by Jerome Mandrillon
Harmonic content of the C400 cyclotron
Harmonic amplitudes
Flutter F and F’
Phase-derivatives rdn/dr almost independent on n
4 alternatives for
’= rd/dr
H4 dominant

## Slide 14: Benchmark against IBA/NHa C400 carbon therapy cyclotron (2)
radial tune
Total: 1+m’+F-terms
F-terms only
Good agreement between closed orbit code (CO) and analytical results for the « F-terms only » case on the right give confidence in correctness of our approach
The non-relativistic approach (as used in HV-paper) is not precise at higher energies and therefore not good enough to predict the 2nr=N resonance stopband accurately

## Slide 15: Results (vertical tune)
The EO is not a circle: this changes the pole face angles at the sector entrance and exit. We can correct for this.
This gives the black curve, which agrees very well with CO
The vertical tune is very sensitive to the precise definition of the harmonic phase derivative ’= rd/dr. This is due to the fact that the bN term dominates at higher energies and that nz is the difference between two « large » numbers.
Blue = closed orbit (CO)
Red=azimuth where B is maximum
Orange= phase of harmonic 4
Green = average of sector edges

## Slide 16: Results (2nr = N stopband)
Stopband coefficients depend only on N
O(f0)
O(f1)
O(f2)

## Slide 17: Cyclotron stability region
Vertical focusing limit (nz=0, dashed curve) and resonance limit (g1, solid curve) as function of flutter F (logaritmic scale) for a number of the sector spiral angles 
Focusing limit monotonically increases with F and 
2nr=N limit monotonically decreases with F and 
Stable area is area below both limits (green area in N=4, =80° plot)
The intersections between focusing and resonance limits represents the energy limit for a given symmetry number N and a given spiral angle 
These are the solid dots in the plot.

## Slide 18: Energy limits
Our result for 𝑁 = 3 agrees very well with the result found by King and Walkinshaw (Ref. 4) who report, in their study on the conversion of the Harwell synchrocyclotron, a proton energy limit of 190 MeV for a spiral angle of about 75°.
For N=4 and a spiral angle of 75° an energy limit of about 450 MeV/u is predicted

## Slide 19: Example for a 230 MeV/u H2+ magnet study with N=3
Here the resonance sets in at E= 187.5 MeV/u (r=48.2 cm)
Spiral angle =79.5° and F=0.0074 with nz=0.27
Our table shows an energy limit of 198 MeV and a flutter of 0.0072
Correcting for the non-zero vertical tune
We find a stopband energy limit of 186.5 MeV/u, very close to the numerical value
tunes:
nr = black
2nz=red
solid = closed orbit
dashed=analytical
field modulation:
solid = flutter F
dashed=spiral angle 

## Slide 20: Conclusion
This work determines the minimum number of sectors that are needed for obtaining a given top energy with a compact isochronous cyclotron.
It also provides the best tradeoff between spiral angle and flutter.
The provided equations, graphs and tables should be useful especially for the conceptual and/or preliminary design of a new cyclotron.
More numerical benchmarks are foreseen, to explore the applicability of the model

## Slide 21
YOUR QUESTIONS ARE WELCOME

## Slide 22: For any question or specific request, please contact your Marketing Team or Corporate Communication

## Slide 23: Important references
Earlier publications covering aspects of the same subject are:
  Ref. 4: N. M. King and, W. Walkinshaw, ‘Spiral Ridge Cyclotron Particle Dynamics Applied to Conversion of the Harwell Synchrocyclotron’, in Nuclear Instruments and Methods, vol. 2, pp. 287-298, 1958.
  Ref. 5: V. I. Danilov, Yu. N. Denisov, V. P. Dmitrievsk., V. P. Dzhelepov, A. A. Glazov et al., ‘Cyclotron With Space Variation Of The Magnetic Field’, in Proc. 2nd Int. Conf. High-Energy Accelerators and Instrumentation, HEACC 1959, CERN, Geneva, Switzerland, September 14-19, 1959, pp. 211-226.
  Ref. 6: M. M. Gordon, ‘Orbit Properties of the Isochronous Cyclotron Ring with Radial Sectors’, in Anals of Physics, vol. 50, pp. 571-597, 1968.
In our paper we use general Hamiltonian approach to the problem

## Slide 24: Results (isochronous field)
relation g=g(r):
Isochronous field:

## Slide 25: Energy dependence of coefficients
Normalized horizontal scale:
Max scale of 0.6 corresponds with 60% of resonance limit at zero flutter
When ignoring cross-terms between average field radial derivatives and the AVF part, (non-relativistic limit) we would obtain constant value (=1) for all cases
Example
horizontal tune:
Strong dependence of coefficients on energy