## Slide 1: Stripping Extraction and Lorentz Dissociation
Hui Wen Koay
TRIUMF

## Slide 2: Outlines
Introduction
Lorentz Dissociation
Conclusion and prospects

## Slide 3: Introduction
Electrostatic extraction | Stripping extraction
 | etc.
No magnetic field or energy limit from Lorentz dissociation A large final turn separation and small beam size is needed Activation from beam loss | Turn separation is not necessary A limited magnetic field and maximum energy (to prevent a large Lorentz loss) Regular replacement of extraction foil
PSI, iThemba, RIKEN etc. Commercial cyclotrons: IBA-C235 | TRIUMF, Deaalus(plan) Commercial cyclotrons: TR30, IBA-Cyclone 30 etc.
Electrostatic extraction | Stripping extraction
No magnetic field or energy limit from Lorentz dissociation A large final turn separation and small beam size is needed Activation from beam loss | Turn separation is not necessary A limited magnetic field and maximum energy (to prevent a large Lorentz loss) Regular replacement of extraction foil
PSI, iThemba, RIKEN etc. Commercial cyclotrons: IBA-C235 | 

## Slide 4
Stripping Extraction

## Slide 5: What is Lorentz dissociation??

## Slide 6: Equivalent Electric Field

## Slide 7: WKB Approximation
e
e

## Slide 8: Lifetime of H-
Experimental lifetime of H-,
Vs/m ;
V/m (Keating et. al.)
Integrating it throughout acceleration, the survival fraction per distance () becomes:
The integrated fractional loss throughout acceleration is

## Slide 9: Example: Lorentz Dissociation of H-
5% at 520 MeV
Closed to the loss in TRIUMF cyclotron

## Slide 10: Power Loss Limit
Power loss limit of a proton beam W/m for hands-on maintenance
Losses are usually spread along the inside surface of the outer wall of the vacuum chamber.
Taking the circumference of the vacuum wall to be , where the radius is the radius at the highest energy

## Slide 11: Lorentz Dissociation of H-
Dashed lines: Power loss limit at 1 mA
Solid line: Lorentz dissociation at respective B
Blue dots: Max allowed energy for hands-on maintanence

## Slide 12: Outlines
Introduction
Lorentz Dissociation
Conclusion and prospects

## Slide 13: General Introduction of H2+
Binding energy 2.7 eV
Internuclear distance
Mainly pre-dissociate through
Lack of experimental verification of Lorentz loss of
H+
H+
e

## Slide 14: Theoretical lifetime of H2+
*Only J=m=0 state is considered (no rotation)
John R. Hiskes (1961) Phy Rev 122-4

## Slide 15: State Population of H2+

## Slide 16: Lorentz Dissociation of H2+

## Slide 17: Lorentz Dissociation of H2+
Dashed lines: Power loss limit at 1 mA
Solid line: Lorentz dissociation at respective B
Blue dots: Max allowed energy for hands-on maintanence

## Slide 18: Lorentz Dissociation of H2+
Dashed lines: Power loss limit at 100 μA
Solid line: Lorentz dissociation at respective B
Blue dots: Max allowed energy for hands-on maintanence

## Slide 19: Outlines
Introduction
Lorentz Dissociation
Conclusion and prospects

## Slide 20: General Introduction of H3+
First detected in 1911 by J. J. Thomson
Binding energy 4.5 eV (7 times of H-)
Internuclear distance
Main structure is an equilateral triangle
No permanent dipole moment
Formed from the exothermic reaction
(1) Breathing (symmetry) mode (A1, A2)
(2) Bending mode -Doubly degenerate (E)
2 Vibrational modes

## Slide 21: Evidence: Lorentz Dissociation of H3+ at DCX-1
Equivalent electric field within the plasma region was 33 to 48 kV/cm
Evidence of Lorentz trapping
G.R. Haste et al 1965 Nucl. Fusion 5 164

## Slide 22: Potential Energy Surface
Reckzügel et. Al. (1995) J. Chem. Phys., Vol. 102, No. 19
MV/cm
MV/cm
MV/cm
MV/cm

## Slide 23: Dissociation Energy of H3+
Fitting the dissociation energy from previous graph:
Example: At 1 GeV/u in a 3 T field, MV/cm, eV. Any excited state with energy greater than 4 eV will dissociate

## Slide 24: State population of H3+
V.G. Anicich et. al. International Journal of Mass Spectrometry and Ion Processes, 55(2):189–215, 1984

## Slide 25: Estimated Lorentz Dissociation of H3+
Assume the Hamiltonian is similar to that of the heteronuclear molecules by Hiskes et. al:
Dashed lines: Power loss limit at 1 mA
Solid line: Lorentz dissociation at respective B
Blue dots: Max allowed energy for hands-on maintanence

## Slide 26: Conclusions
Overall, the order of stability goes from H3+>H2+>H- at energy greater than 100 MeV/u.
At low energy < 100 MeV/u, H- is the most cost efficient; while H3+ is the most stable at energy higher than 100 MeV/u.
In general, a larger machine is more conducive for stripping extraction at a high power due to a lower Lorentz dissociation at a lower B and a larger power loss permissible for hands-on maintenance.
Initial state distribution from the ion source is the game-changer: important to be able to tune it accordingly.

## Slide 27: Prospects
Experimental verification is NECESSARY, especially for H2+ and H3+, as many practical factors have been omitted.

## Slide 28: Thank you!