## Slide 1: Design of a multi-harmonic buncher for TRIUMF 500 MeV cyclotron
S. Saminathan, R. Baartman, Y. Bylinski, M. Ilagan, P. Jung, O. Law, R. E. Laxdal, M. Marchetto, T. Planche, V. Zvyagintsev
TRIUMF, Vancouver, BC, CANADA
CYC2022, Beijing, China

## Slide 2
Overview
Motivation
Status on the injection beamline upgrade program
Present buncher system
New buncher system
Summary and outlook

## Slide 3
Motivation
Injection beamline upgrade program
Fig. 1: TRIUMF 500 MeV H- cyclotron
Beam species | H-
Beam energy | 300 keV
Maximum beam intensity | 1 mA
Duty cycle | 0.1 % to 99 %
Bunching frequency | 23.06 MHz
Growing demand for higher proton beams out of cyclotron (Total extracted current ~400 µA)
To ARIEL
Injection of high intense high brightness beams
Reliable operation of injection beamline
Table:1 Basic beam requirements

## Slide 4: Status on the injection upgrade program
Current deliverables:
  New ion source terminal (I2)
  New beam transport section from I2 to I1
  Transport section upgrade from I1 to vertical section
  Bunching systems
  Machine protection
  Magnetic stray field compensation
  Diagnostics
  Controls (EPICS)
2024-2025
2010-2011*
Existing ion source terminal
New ion source terminal
Fig. 2: Ion source and injection system
New multi-harmonic buncher
Proposed
Re-buncher
* R. Baartman, ``Optics Design of the ISIS Vertical Section Replacement", TRI-DN-09-11, TRIUMF document-22849

## Slide 5
Present buncher system
Fig. 5: Calculated electric field along the axis of the buncher with an applied potential of 1 V.
Fig. 4: Calculated electrostatic potential contour by using the code POISSON/SUPERFISH
Aperture radius | 2.54 cm
1st harmonic | 23.06 MHz
2nd harmonic | 46.12 MHz
beta•lambda | 33.53 cm
400 cm
1700 cm
2nd harmonics
1st harmonics
Cyclotron injection
Fig. 3: Present 46 MHz 2nd buncher
Table:2 Present buncher *
* Baartman, R A and Dutto, G and Schmor, P W, "The TRIUMF high efficiency beambunching system", Proceedings of the Tenth International Conference on Cyclotrons and their Applications, East Lansing, Michigan, US, 1984

## Slide 6
A novel multi-harmonic buncher
Fig. 8: Calculated electric field along the axis of the buncher with an applied potential of 1 V.
Fig. 7: Calculated electrostatic potential contour by using the code COMSOL
Fig. 6: A concept layout of the multi-harmonic buncher cavity *
Courtesy: * proposed by V. Zvyangintsev
1st & 3rd harmonics
2nd harmonics
Table:3 New multi-buncher
Aperture radius | 1.27 cm
1st harmonic | 23.06 MHz
2nd harmonic | 46.12 MHz
3rd harmonic | 69.18 MHz
Re-buncher | 23.06 MHz

## Slide 7
Initial particle distributions
Fig. 9: Calculated initial longitudinal phase-space
Fig. 10: Calculated initial transverse phase-space
Simulation tool
Particle-in-cell code WARP *
A. Friedman et al., Computational Methods in the Warp Code Framework for Kinetic Simulations of Particle Beams and Plasmas, in IEEE Transactions on Plasma Science, vol. 42, no. 5, pp. 1321-1334, May 2014

## Slide 8
Present 1st & 2nd harmonic buncher (I = 650 µA)
Fig. 13: Calculated transverse phase-space
Fig. 11: Calculated longitudinal phase-space
Fig. 12: Calculated beam envelope (2RMS, positive for x, negative for y, longitudinal for z)

## Slide 9
New multi-harmonic (I = 650 µA)
Fig. 14: Calculated longitudinal phase-space
Fig. 15: Calculated beam envelope (2RMS, positive for x, negative for y, longitudinal for z)
Fig. 16: Calculated transverse phase-space

## Slide 10
New multi-harmonic with re-buncher (I = 650 µA)
Fig. 14: Calculated longitudinal phase-space
Fig. 15: Calculated beam envelope (2RMS, positive for x, negative for y, longitudinal for z)
Fig. 16: Calculated transverse phase-space

## Slide 11
New multi-harmonic with re-buncher (I = 1 mA)
Fig. 17: Calculated longitudinal phase-space
Fig. 18: Calculated beam envelope (2RMS, positive for x, negative for y, longitudinal for z)
Fig. 19: Calculated transverse phase-space

## Slide 12
Summary
A novel multi-harmonic buncher system has been designed, which will be operated by up to three harmonics.
The beam dynamics studies have been performed, including the space-charge effects using the particle-in-cell code WARP.
The new bunching system will be a combination of multi-harmonic and re-buncher for transporting beam injection beamline intensity higher than 500 µA.
Simulation results of longitudinal beam dynamics are presented for transporting beam intensity up to 1 mA.
The bunching efficiency of this system is about 67 % (± 25 deg. and Δp/p = ± 0.5 %) at 1 mA injection line current could support up to 650 µA extracted currents

## Slide 13: Thank you Merci
Follow us @TRIUMFLab
www.triumf.ca